Tender Descriptive:

- PONZI TSA TOS 2+1 -

ANTI-PANIC TELESCOPIC AUTOMATIC DOOR WITH A 2 SLIDING WINGS AND 1 SEMI-FIXED WING ROUNDED ACCIDENT PREVENTION PONZI 50mm PROFILES

TSA TOS 2 + 1 ANTI-PANIC TELESCOPIC DOOR

ROUNDED ACCIDENT PREVENTION PONZI SERIES 50mm PROFILES

Made of three doors, one semi-fixed and two sliding parallel and simultaneously overlapping on the fixed element.

The door are made of extruded aluminum alloy profiles of mm. 50 - our rounded accident-prevention series - surface finish made with anodised electro-coloring (with color to choose from our sample book) fire-resistant process, 8/9 mm thick laminated accident-prevention glass composed of two 4 mm clear transparent float plates with interposed p.v.b movie from mm. 0.76. Sliding guides, made of special aluminum alloy with anodised electro-colour surface treatment with perfect degree of silence.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys per door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable box in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS)

• N. 2 combined radar (motion and presence sensor).

N...... dimensions da mm……… x mm.H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it