Tender Descriptive:

- PONZI RONDINA	-

CIRCULAR SLIDING CURVED DOOR

CIRCULAR SLIDING CURVE DOOR PONZI RONDINA

Made with circumferential sector doors, of which the two central ones slide automatically and the two fixed side parts. The fixed and movable side doors are made of special extruded aluminium profiles of 20/30 mm and curved to perfect radius, surface finish made with RAL color fire treatment (to be chosen from our sample book) accident prevention laminated glass 8/9 composed of two transparent clear float plates of mm. 4 + 4 with interposed film p.v.b. from

mm. 0.76. Inspectable box H = mm 220.

The Rondina microprocessor-controlled mechanism, with a basic automatic mechanism with rubber support on

LAURAMID guide wheels and silent sliding toothed belts, consists of:

•  N. 1 Gear Motor

•  N. 1 Transformer, 220 / 34-50 Volt power supply (for general low voltage).

•  N. 1 Micro authorizing officer (programme card)

•  N. 1 extruded aluminum track.

•  N. 1 Standard function selector (BDE)

•  N. 2 Movement and presence sensors.

•  N. 1 Emergency battery (guarantes 1 opening of the doors in case of power failure)

•  N.1 Locking with electric lock operated by the selector

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it