Tender Descriptive:

- PONZI TSA 2 -

TELESCOPIC SLIDING DOOR WITH 2 SLIDING WINGS COPLANAR PONZI SERIES 32mm PROFILES

TELESCOPIC SLIDING DOOR PONZI TSA 2

COPLANAR PONZI SERIES 32mm

Made of two sliding doors parallel to and simultaneously overlapping on the fixed element.

The wings are made of extruded alumium of mm.32 our rounded accident prevention series- surface finish made with a fire painting or anodic electro-coloring process (color to choose from our sample book), laminated accident-proof glass 8/9 mm thick. (Also available with insulating double glazing up to a maximum thickness of 15 mm). Sliding alloy with anodised electro-colour surface treatment with perfect degree of silence.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys per door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

• Inspectable casing in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS)

• N. 2 combined radar (motion and presence sensor).

N...... dimensions da mm……… x mm.H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it