Tender Descriptive:

- PONZI TSA 2 -

TELESCOPIC SLIDING DOOR WITH 2 SLIDING WINGS ROUNDED ACCIDENT PREVENTION PONZI SERIES 50mm PROFILES

PONZI TSA 2 TELESCOPIC SLIDING DOOR

PROFILES PONZI SERIES 50mm STORED ACCIDENT PREVENTION

Made of two sliding doors parallel to and simultaneously overlapping on the fixed element.

The wings are made of extruded alumium alloy profiles of mm 50 our rouneded accident prevention

series-surface finish made with anodised electro-coloring (with color to choose from our sample book) fire-resistant process 8/9 mm thick laminated accident prevention glass composed of two 4 mm clear transparent float plates with interposed p.v.b movie from mm 0.76 . (Also available with insulating double glazing up to a maximum thickness of 36 mm) Sliding guides, made of special aluminum alloy with anodised electro-colour surface treatment with perfect degree of silence.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys per door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

• Inspectable casing in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS)

• N. 2 combined radar (motion and presence sensor).

N...... dimensions da mm……… x mm.H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it