# Text boxes

Tender Descriptive:

- PONZI TSA 2+1-

TELESCOPIC  SLIDING  DOOR     WITH  A    2  SLIDING  WINGS AND  1      FIXED   WING

PROFILES    PONZI     SERIES    32 mm     COPLANAR

PONZI  TSA      2 + 1    TELESCOPIC  AUTOMATIC  DOOR

PROFILES  PONZI  SERIES  32 mm      COPLANAR

Made of three doors, two of which slide parallel and simultaneously overlapping stand on the fixed element.

The doors are made of extruded aluminium alloy profiles of mm. 32 our rounded accident-prevention series - surface finish made with anodised electro-colouring (with colour to choose from our sample book) fire-resistant process, 8/9 mm thick laminated accident-prevention glass composed of two 4 mm clear transparent float plates with interposed p.v.b movie from mm. 0.76. (Also available with insulating double glazing up to a maximum thickness of 15 mm). Sliding guides, made of special aluminium alloy with anodised electro-colour surface treatment with perfect degree of silence.

The automatism consists of:

- N. 1 Low voltage gear motor.

- N. 1 stabilized power supply.

- N. 1 Microprocessor control board.

- N. 1 extruded aluminum track.

- N. 2 carrier trolleys per door.

- N. 1 adapter profile for suspension leaf.

- N. 1 Multi-function battery pack

- N. 1 bistable electric lock.

- Inspectable casing in extruded aluminum (H = 155 mm).

- N. 1 Function selector with 5 positions (KS)

- N. 2 combined radar (motion and presence sensor).

N...... dimensions da mm……… x mm.H.

Srl

Seat:

48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25 Tel. +39 02 8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it

info@ponzi-in.it