Tender Descriptive:

- PONZI TSA 4 -

TELESCOPIC SLIDING DOOR WITH 4 WINGS REDUCED SECTION PONZI SERIES SLIM 20mm PROFILES

TELESCOPIC SLIDING DOOR WITH 4 WINGS

PROFILES PONZI SERIES SLIM 20 mm WITH REDUCED SECTION

Made of four sliding doors parallel and simultaneously (two by two) a overlap on the fixed element.

The shutters are made of extruded aluminium alloy profiles of mm 20 our rounded accident prevention series - surface finish made with anodized electro-coloured fire-coating process (colour to choose from our sample book), 8/9 mm thick laminated accident-prevention glass composed of two 4 mm clear transparent float plates with interposed p.v.b film from mm. 0.76. (Also available with insulating double glazing up to a maximum thickness of 12 mm). Sliding guides, made of special aluminium alloy with anodised electro-colour surface treatment with perfect degree of silence.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys per door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable casing in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS)

• N. 2 combined radar (motion and presence sensor).

N...... dimensions da mm……… x mm.H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it