Tender Descriptive:

- PONZI ASD 1+1

AUTOMATIC SLIDING DOOR WITH 1 SLIDING WING AND 1 FIXED WING PROFILES PONZI SERIES THERMAL CUT

AUTOMATIC SLIDING DOOR PONZI ASD 1+1

PROFILES PONZI SERIES THERMAL CUT

Made of two mirrors, one of which is fixed and one that can be opened automatically.

The door is made of reduced profiles in thermal break aluminum alloy - rounded Ponzi accident-prevention series - surface finish made with an oven-painted or anodic electrolytic treatment (color to choose from our sample book), laminated accident-proof glass 44 mm thick 8/9 composed of two 4 mm clear transparent float plates with interposed pvb film from 0.76 mm. (Also available with insulating double glazing up to a maximum thickness of 45 mm). Special gaskets with relative counter-profiles for thermo-acoustic sealing.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 Stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys for door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable box in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS).

• N. 2 combined radar (motion and presence sensor).

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it