Tender Descriptive:

- PONZI ASD 4 -

AUTOMATIC SLIDING DOOR WITH TWO SLIDING WING AND TWO FIXED WINGS

PROFILES PONZI SERIES SLIM 20 mm WITH REDUCED SECTION

PONZI ASD 4 SLIDING DOOR

PROFILES PONZI SERIES SLIM 20 mm WITH REDUCED SECTION

The wings are made of extruded profiles in 20 mm aluminum alloy - Ponzi series, rounded, accident-prevention-surface finish made with an oven-painted or anodised electrolytic treatment (color to choose from our sample book), laminated accident-prevention glass 44 mm 8 / 9 composed of two 4 mm clear transparent float plates with interposed pvb film from 0.76 mm (Also available with insulating double glazing up to a maximum thickness

of 12 mm). Special gaskets with relative counter-profiles for thermo-acoustic sealing.

The automatism consists of:

•  N. 1 Low voltage gear motor.

•  N. 1 Stabilized power supply.

•  N. 1 Microprocessor control board.

•  N. 1 extruded aluminum track.

•  N. 2 carrier trolleys for door.

•  N. 1 adapter profile for suspension leaf.

•  N. 1 Multi-function battery pack

•  N. 1 bistable electric lock.

•  Inspectable box in extruded aluminum (H = 155 mm).

•  N. 1 Function selector with 5 positions (KS).

•  N. 2 Combined radar (motion and presence sensor).

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it