Tender Descriptive:

- PONZI LOWERED ARCH TOS -

SECTOR CURVED DOOR OF ANTI-PANIC CIRCUMFERENCE

SECTOR CURVED DOOR OF ANTI-PANIC CIRCUMFERENCE

PONZI LOWERED ARCH TOS

Made of four mirrors with circumferential sectors, curved to perfect radius, of which the semi-fixed side panels and the central ones that open automatically to slide with the PONZI STA 20 mechanism.

The semi-fixed and sliding side doors are made of steel sections covered with aluminum, finishing surface made with fire - retardant RAL color treatment (to be chosen from our bundle), 8/9 mm thick accident-prevention laminated glass composed of two clear transparent mm float plates. 4 + 4 with interposed film p.v.b. from mm 0.76. Special sealing gaskets with relative counter-profiles. The mechanism consists of: DSTA type microprocessor, mounted on a self-supporting steel support; suspension with carriages on high-slip ball bearings; lauramid outer crown; transmission realized by means

of a toothed belt in special canvas rubber. Curved external skirt H = mm 220 covering the beam and the sliding track.

The automatism consists of:

•  N. 1 Gear Motor

•  N. 1 Transformer, power supply (220 / V-50 HZ. In input, 24V operation)

•  N. 1 Micro authorizing offrcer (program card)

•  N. 1 extruded aluminum track.

•  N. 1 Standard function selector (BDE)

•  N. 2 Movement and presence sensors.

•  N. 1 Emergency battery (guarantes 1 opening of the doors in case of power failure)

•  N.1 Locking with electric lock operated by the selector

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it