# Text boxes

Specifications description:

- PONZI PG 3 -

REVOLVING DOOR WITH 3 LEAVES

MANUAL REVOLVING DOOR WITH 3 LEAVES PONZI PG3

Composed by:

• Semi-circular fixed side walls built with extruded aluminum alloy profiles usually made for rotating automation systems, surface finish made with RAL color fire painting treatment (to be chosen from our samples), laminated glass composed of two clear transparent float sheets of mm. 4 + 4 with interposed film p.v.b. from mm. 0.76;

• 200 mm high circular top hat built with an extruded alloy section aluminum specially made for revolving automation systems, both in the coplanar and external version (at your choice), complete with dust-proof upper panel;

• THREE SWIVEL DOORS WITH MANUAL OPERATION, fixed on a central rotating axis, made of extruded aluminum alloy profiles specially made for rotating automation systems, anodized or painted (RAL color of your choice from our samples), laminated glass made up of two sheets clear transparent float mm. 4 + 4 with interposed film p.v.b. from mm. 0.76;

• Brushes and seals mm. 40, made of antistatic technical material, placed on three sides for optimal airtightness in any position of the doors;

• MANUAL LOCK with safety cylinder for manual mechanical locking of the door.

N………….size  from  mm……… x mm………..H.

AUTOMATIC REVOLVING DOOR WITH 3 LEAVES PONZI PG3

The automatic version of the door is complete with a device for the AUTOMATIC function, provided with electromechanical automation that comes into operation when a user is near the door, accompanying the entry and / or exit path and repositioning the leaves always in the position optimal for perfect closure, complete with:

• 24 Volt DC motor

• Electrical panel with low voltage microprocessor control unit Main power supply: 230 Va.c., • 50 Hz, 0.3 kW (max)

• 5-position electromechanical function selector (AUTOMATIC / PUSH & GO)

ONE-WAY / MANUAL / NIGHT DISABLING

• N. 2 movement sensors for the opening impulse

• N. 1 red emergency STOP mushroom pushbutton positioned on the exit riser

• N. 2 sensitive rubber safety edges located at each end of the fixed curved parts. Activating one of them stops the rotation of the leaves.

• N. 2 active infrared safety sensors for slowing down and / or stopping near the two sensitive edges

• N. 1 sensitive rubber safety edge located horizontally at the base of each revolving door. The activation of one of them stops the rotation of the doors. (active door sill)

• N. 1 sensitive rubber safety edge located vertically on the external upright of each passive / active rotating mobile leaf

N...... size  from  mm……… x mm.	H.

ADDITIONAL SECURITY OPTIONS:

- N. 1 active infrared safety presence sensor located horizontally on the upper crosspiece of each revolving door. The activation of one of them slows down or stops the rotation of the doors.

- N. 2 disabled buttons (one for each riser: input and output) which activate rotation at low speed

OPZIONI ADDIZIONALI DI SICUREZZA ANTI-EFFRAZIONE:

- Mechanical lock with safety cylinder for manual mechanical closing of the door (installed on the revolving doors)

- Electronically controlled electric lock, installed inside the automation: acts on the transmission, blocking rotation. Fail-safe type (UNLOCK in the absence of voltage) or fail-secure (BLOCK in the absence of voltage)

- Electronically controlled electric lock, installed inside the automation: it acts on the revolving door, locking it directly. Fail-safe type (UNLOCK in the absence of voltage) or fail-secure (BLOCK in the absence of voltage)

- Additional COURTESY OPTIONS (AUTOMATIC version only)

- Led spotlights, spotlight frame color white / silver / gold

ADDITIONAL OPTIONS:

- Electronic function selector with display showing the functional status selected and any alarm messages. Available functions: NIGHT LOCK / AUTOMATIC / PUSH & GO / AUTOMATIC EXIT ONLY / AUTOMATIC ENTRY ONLY / CONTINUOUS ROTATION AT LOW SPEED / CONTINUOUS ROTATION AT NORMAL / MANUAL SPEED.

- App on smartphone for total control of the door: selection of functions (8) and display of any alarm messages

Integration of the door into the Internet network (access to the LAN must be made available) for remote control and surveillance by the tenant (via smartphone and PC) and - if required - control, firmware update and remote maintenance by of the manufacturer.