Tender Descriptive:

- PONZI FDA TOS -

AUTOMATIC DOOR WITH ANTI-PANIC FOLDING SIDE COLLECTIONS

FDA TOS ANTI-PANIC FOLDING AUTOMATIC DOOR

Made of four folding doors that open automatically (two on each side).

The doors will be built with extruded aluminum alloy profiles - surface finish realized with anodic electro-coloring treatment or fire-painting (colour to choose from our sample collection), complete with upper and lower pins rotating on ball bearings and special hinges with very high resistance and seal; laminated safety glass 55 mm thick 10/11 composed of two transparent clear float plates of mm.5 with interposed film p.v.b. from mm. 0.76. Perimeter seals for a perfect thermo-acoustic seal. Folding door mechanism controlled by a microprocessor FTA 107 TOS, mounted on an aluminum support, internal lever system mounted on highly silent ball bearings,

220 / V 50Hz power supply, 24V operation.

The Rondina microprocessor-controlled mechanism, with a basic automatic mechanism with rubber support on

LAURAMID guide wheels and silent sliding toothed belts, consists of:

•  N. 1 Gear Motor

•  N. 1 Transformer,power supply

•  N. 1 Micro authorizing officer (programme card)

•  N. 1 extruded aluminum track.

•  N. 1 Standard function selector (BDE)

•  N. 2 Movement and presence sensors.

•  N. 1 Emergency battery (guarantes 1 opening of the doors in case of power failure)

•  N.1 Locking with electric lock operated by the selector

•  Sliding accessories.

•  Inspectable box in extruded aluminium H = mm. 180

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it