Tender Descriptive:

- PONZI ALU GLASS PARALLELO -

MANUAL HOSPITAL SLIDING DOOR ALU GLASS PARALLEL

SWING DOOR PONZI ALU TYPE, MADE IN ONE / TWO SWING LEAVES.

Built with extruded profiles in ENAW 6060 aluminum alloy according to UNI 9006/1 rules and accessories belonging to the ALU PONZI system. The profiles will be anodised, silver color ARS1, class 15 micron according to UNI4522 regulation.

The door is complete with:

•Filling on three sides, with complementary extruded profiles that can be coupled together, suitable for wrapping the entire shoulder of the wall for a thickness from 100 to 150 mm (for higher wall thicknesses it will be compensated separately with extra charge).

•Door leaf, surrounded on all four sides by a 45/50 mm aluminum frame with rounded edges, 44.2 transparent

laminated glass

• Accessories: hook lock with Yale type cylinder, pair of round diameter 35 handle recessed on the upright

• Double door gasket in EPDM elastomer

N...... dimensions from mm……… x mm. H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it