Description of specifications:

- PONZI TOS THERMAL BREAK 4 LEAVES -

AUTOMATIC SLIDING DOOR WITH THERMAL BREAK FOR ESCAPE WAYS,

TWO MOVABLE LEAVES AND TWO FIXED LEAVES

SPECIAL SERIES PROFILES PONZI 65 mm

AUTOMATIC SLIDING DOOR WITH THERMAL BREAK

FOR ESCAPE ROUTES PONZI TOS 4

SPECIAL SERIES PROFILES PONZI 65mm - LATEST GENERATION

AUTOMATIC SLIDING DOOR PONZI AS3 TOS with THERMAL BREAK for USE ON ESCAPE ROUTES, made of four panels, of which the central ones can be opened automatically by sliding and opened by single push, the lateral SEMIFIXED open by simple push. The doors are built in exclusive 65 mm extruded thermal break profiles - our exclusive series, specially designed for use in automatic doors - surface finish made with oven painting or anodic electro-coloring treatment (color of your choice from our sample book), accident prevention stratified double glazing with total thickness up to 45 mm, in a composition correlated to the required / necessary thermal performance. Complete with special gaskets.

The automation consists of:

• N. 1 low voltage gearmotor.

• N. 1 stabilized power supply.

• N. 1 microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrying trolleys per door.

• N. 1 Adapter profile for suspension door.

• N. 1 multifunction battery pack

• N. 1 bistable electric lock.

• Inspectionable box in extruded aluminum (h = mm. 155).

• N. 1 5-position function selector (KS).

• N. 2 Radar (motion and presence sensor).

TOTAL BREAK-OUT TOS PANIC DEVICE:

In the event of an emergency, the central sliding doors and the semi-fixed side doors - in normal operation - can be hinged outwards with a simple pressure in any point of the doors, even if in motion. The system, by means of guides fixed to the floor, allows the lateral collection of the four leaves, (two on each side) with automatic deactivation of the function until the operating function is restored and is completed by sturdy interlocking profiles with release along the entire length of the door (not through contact bridges) .. This opening system, made with thermal break profiles exclusively by PONZI srl and covered by a patent, assumes the function of Panic Device and Safety Exit and has been tested by Istituto Giordano S.p.A. resulting in compliance with the most recent regulations regarding automatic pedestrian closures installed on escape routes. (pr. EN 16005; Ministerial Decree 10 March 1998 - annex III).

N...... dimensions  from  mm……… x mm.	H.