Description of specifications:

- PONZI TOS 1+1-

AUTOMATIC SLIDING DOOR FOR ESCAPE ROUTES AND A SLIDING AND A SEMIFIXED WING ROUNDED ACCIDENT PREVENTION PONZI SERIES 50mm PROFILES

AUTOMATIC SLIDING DOOR FOR ESCAPE ROUTES TOS 1 + 1 ROUNDED ACCIDENT PREVENTION PONZI SERIES 50mm PROFILES

Made of two mirrors, one of which is semi-fixed and one that can be opened automatically.

The doors are made of 50 mm extruded aluminum alloy profiles - our rounded accident-prevention series - surface finish made with an oven-painted or anodised electrolytic treatment (color to choose from our sample book), 8 mm thick 9 composed of two 4 mm clear transparent float plates with pvb film interposed from 0.76 mm. (Also available with insulating double glazing up to a maximum thickness of 36 mm). Complete with special seals.

The automatism consists of:

N. 1 Low voltage gear motor.

N. 1 stabilized power supply.

N. 1 Microprocessor control board.

N. 1 extruded aluminum track.

N. 2 carrier trolleys per door.

N. 1 adapter profile for suspension leaf.

N. 1 Multi-function battery pack

N. 1 bistable electric lock.

Inspectable casing in extruded aluminum (H = 155 mm).

N. 1 Function selector with 5 positions (KS).

N. 2 combined radar (motion and presence sensor).

TOS BREACHING ANTI-PANIC DEVICE

In the event of an emergency, the sliding leaf- in normal operation - can be tilted to the outside in any position it is, with a simple pressure at any point of the same, even when in motion.

The system, by means of guides fixed to the floor, allows the leaf to swing open, disabling the automatic function until the function is restored. This opening system therefore assumes the function of an anti-panic device and a safety exit and complies with the most recent regulations on pedestrian automatic closures installed on escape routes (EN 16005; DM 10 March 1998 - annex III; Legislative Decree 81/2008).

NB: To carry out the breakout function for the escape route even with the door moving, it is essential that the mechanism is positioned outside the compartment.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25 Tel. +39 02 8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it	info@ponzi-in.it