Tender Descriptive:

- PONZI TOS 4 -

ROUNDED ACCIDENT PREVENTION PONZI SERIES 50 mm PROFILES

PONZI TOS 4 AUTOMATIC SLIDING DOOR FOR ESCAPE ROUTES PROFILES PONZI SERIES 50 mm STORED ACCIDENT PREVENTION

Made of four mirrors, of which the semi-fixed side panels and the central ones that open automatically.The shutters are made of 50 mm extruded aluminum alloy profiles - rounded Ponzi accident-prevention series - surface finish made with an oven-painted or anodic electrolytic treatment (color to choose from our sample book), laminated accident-proof glass 44 mm 8 / 9 composed of two 4 mm clear transparent float plates with interposed pvb film from 0.76 mm. (Also available with insulating double glazing up to a maximum thickness of 36 mm). Special gaskets with relative counter-profiles for thermo - acoustic sealing.

The automatism consists of:

• N. 1 Low voltage gear motor.

• N. 1 stabilized power supply.

• N. 1 Microprocessor control board.

• N. 1 extruded aluminum track.

• N. 2 carrier trolleys per door.

• N. 1 adapter profile for suspension leaf.

• N. 1 Multi-function battery pack

• N. 1 bistable electric lock.

Inspectable casing in extruded aluminum (H = 155 mm).

• N. 1 Function selector with 5 positions (KS)

• N. 2 combined radar (motion and presence sensor).

TOTAL BREACHING PANIC DEVICE

In the event of an emergency, the central sliding doors and the semi-fixed side doors - in normal operation - can be opened against the outside with a simple pressure at any point of the two sliding doors even if in movement. The system, by means of guides fixed to the floor, allows the lateral collection of the four doors, (two on each side) with the automatic function being disengaged until the function is restored and is completed by sturdy interlocking profiles with release along the entire length of the door. 'door (not via contact points). This opening system therefore assumes the function of an anti-panic device and a safety exit and has been tested, in accordance with the most recent regulations regarding pedestrian automated closures, by the Giordano S.p.A.

N...... dimensions da mm……… x mm.H.

Srl

Seat:	48031 BAGNARA (RA)

VIA Gramsci, 26/A Tel. +39 0545 76009

Fax +39 0545 76827

P. IVA 02144680390

20123 MILANO

Viale G. D’Annunzio, 25

Tel. +39 02  8394231

Fax +39 02 89422342

00138 ROMA

Via Salaria, 1378

Tel. +39 06 88566005

Fax +39 0688560406

65015 MONTESILVANO (PE)

Via A. Moro, 6

Tel. +39 085 4483020

Fax. +39 085 4455895

www.ponzi-in.it 	info@ponzi-in.it